## Slide 1: USER GUIDE BIKE Tracker
Werner Meihuizen, David Meijer en Remco de groot

## Slide 2: Diagram

## Slide 3: Required components
Sim card with NB-IOT capabilities
Arduino MKR NB 1500
Arduino MKR GPS Shield
Dipole Pentaband Waterproof Antenna
Eslof cable
Flask server to receive and show data.

## Slide 4: Choices
Arduino MKR GPS Shield has built in GPS
Arduino MKR NB 1500 has a sim card slot, the shield can go on top and easy to attach antenna.
Dipole Pentaband Waterproof Antenna cane with the Arduino MKR NB 1500
Flask easy to setup

## Slide 5: Wireless technology
Why NB-IoT?
  Utilizes the cellular network for wide coverage.
  Ensures data transmission regardless of location.
Frequency and Range in Europe:
  Operates on 800MHz or 900MHz bands (2).
  Coverage up to 10 kilometers (2).
Notes: Orthogonal frequency-division multiplexing: multiple carrier frequencies. Used for wideband digital communication. The bit stream is divided into multiple streams. Multiple subcarriers with overlapping spectra. Multiple bits send at the same time.
Singe-Carrier FDMA: change data into symbols and use Discrete Fortier Transformation to change it into frequency signals. The signals are placed into subcarriers. The signals are transformed into waves and send.

## Slide 6: Wireless technology
Key Features of NB-IoT:
  Reusing existing infrastructure for lower power devices.
  Low-power wide-area network (LPWAN).
  Maximum bandwidth: 200kHz (1).
  Downlink speed: Up to 127 kbit/s (1).
  Uplink speed: Up to 159 kbit/s (1).
  Latency: Between 1.6 and 10 seconds (1).
  Half-duplex communication (can’t send and receive simultaneously).
  Transmit power options: 14/20/23 dBm (1).
  Device can be asleep when not sending/receiving data.
  Orthogonal frequency-division multiplexing modulation for downlink(1)
  Single-carrier FDMA modulation for uplink (1)
Notes: Orthogonal frequency-division multiplexing: multiple carrier frequencies. Used for wideband digital communication. The bit stream is divided into multiple streams. Multiple subcarriers with overlapping spectra. Multiple bits send at the same time.
Singe-Carrier FDMA: change data into symbols and use Discrete Fortier Transformation to change it into frequency signals. The signals are placed into subcarriers. The signals are transformed into waves and send.

## Slide 7: Tracker
Use sim card and antenna to connect to NB-IOT network
Arduino MKR GPS Shield to get the coordinates of its current location
The Arduino MKR NB 1500 sends the location data with a timestamp.

## Slide 8: Flask webserver
Receives the location data and saves the timestamp
Data saved in database
When needed data is requested from database
Display data on frontend

## Slide 9: Frontend
JavaScript on a web page
leaflet.js library to display a map
Displays the location of the bike and your own
Place the map using a div
Gets data from flask webserver through an api

## Slide 10: Frontend

## Slide 11: Troubleshooting
Unable to connect to NB-IoT
Sim card works as expected
Low power unless searching for network?
GPS same problem

## Slide 12: Next steps
Fixing connectivity issue
Sending information to webserver
Verifying everything works

## Slide 13: Sources
Wikipedia contributors. Narrowband IoT [Internet]. Wikipedia. 2024. Available from: https://en.wikipedia.org/wiki/Narrowband_IoT
What is Narrowband IoT (NB-IoT): A comprehensive guide [Internet]. A1 Digital. 2024. Available from: https://www.a1.digital/news/what-is-narrowband-iot-a-comprehensive-guide/#:~:text=NB%2DIoT%20frequency%20and%20range,range%20and%20penetrate%20buildings%20better.

## Slide 14: Thank you!
Notes: Orthogonal frequency-division multiplexing: multiple carrier frequencies. Used for wideband digital communication. The bit stream is divided into multiple streams. Multiple subcarriers with overlapping spectra. Multiple bits send at the same time.
Singe-Carrier FDMA: change data into symbols and use Discrete Fortier Transformation to change it into frequency signals. The signals are placed into subcarriers. The signals are transformed into waves and send.